## Slide 1
EE222 High-Speed Low-Power ICs
Spring 2017
Instructor: Sung-Mo “Steve” Kang
Room BE-239
skang@ucsc.edu
(831)502-7052
Acknowledgments- Prof. Eby Friedman of the University of Rochester and Prof. Yusuf Leblebici of EPFL have provided
Lecture materials.

## Slide 2: Time and Place
4:00 to 5:05 PM, M, W, and F
Baskin Engineering Bldg. Room 156

## Slide 3: Course Contents
Technology
Technologies
SemiconductorMaterials
Solid-State
Device Physics
Applications
Computers
IoT, Sensors
Image Processing
Wireless
DSP
Biomedical Apps
 
VLSI IC
Design
Will attempt to integrate technology issues and application issues into the topic of VLSI design
  Which technology for which application?
  Speed, area, power, complexity, I/O interface, especially LOW POWER is critical
  Digital or analog?
  On-chip A/D? Mixed-signal?
  Single large chip or multiple small chips?
  Printed circuit board (PCB), MCM, WSI, 3-D
    - Systems integration issues

## Slide 4: Summary of Course Organization
Introduction- VLSI design issues and technologies
Low Power (LP) CMOS Logic
LP Design Flow
CMOS power dissipation
5. LP Biomedical Circuits and Systems
6. CMOS Circuits Power Basics
Interconnects
Custom Ips, Library
9. Semiconductor Memories
10. Project Proposals
High Speed (HS) Architecture and Timing
Multiple Clock Domains
Synchronous Design
Asynchronous Design
Technology Scaling
Packaging
Reliability
Final Presentations

## Slide 5: Design Methodologies
PLD/FPLD/ Gate Arrays Standard cells Structured Full
PLA/FPGA SOG’s core cells custom custom
Higher complexity
Lower Power
Lower NRE
Longer design time
Higher speed
Lower RE
Higher volume
Semi-custom

## Slide 6: Complexity vs. Year and the Y–Chart
Typical VLSI design flow in three domains (Y-chart representation)
Level of integration versus time, for memory chips and logic chips
1970
1980
1990
2000
–
–
–
–
–















–
–
–
–


100
5 x 107
16M
4M
1M
250K
DEC Alpha
80486
Pentium
64K
1K
16K
4K
4004
8008
8085
104
103
105
8048
8080
68000
68030
32A
8066
80386
Bellmac
68020
68040
80286
80860
106
107
108
 Microprocessor
 Memory
Transistors per die
Source: Intel Corp.
D. D. Gajski (Ed.), Silicon Compilation, Addison Wesley, 1988

## Slide 7: Levels of Design
Levels of design in the tripartite representation
Dan Gajski’s Y-chart
Processor, Memory, switch
Hardware modules
Transistors, contacts, wires
ALUs, MUXs, registers
Gates, flip-flops, cells
Algorithms
Physical Partitions
Clusters
Modules
Floor plans
Layout
Register transfers
Behavioral
domain
Systems
Logic
Transfer functions
Structural
domain
Physical domain

## Slide 8: Performance Issues in VLSI/IC Design and Analysis
What is design in VLSI/IC?
Levels of Abstraction
Technology
Process
Device
Geometric
Circuit
Logic
RTL - structural
Behavioral
Systems
This class will focus here

## Slide 9
Circuit design
Layout design
Logic design
Architecture
definition
Circuit design
Layout design
Fabrication
Behavioral
description
Structural
description
Physical
description
System requirements
and specifications
Architecture level
Physical level
Register transfer level
Testing
Integrated Circuit Design Flow

## Slide 10: A Host of VLSI/IC CAD Problems Exist
Cell generation
Testability improvement
Automated layout: 1-D, 2-D, and hierarchical
Logic optimization
Logic synthesis
RTL synthesis
HDL/Behavioral synthesis
Back annotation
Timing analysis
Circuit simulation and modeling
Mixed mode simulation
Sequential machine optimization and synthesis
Register allocation
Process simulation, modeling and tolerance
Device simulation
Analog synthesis,Test
Analog simulation
Tool integration

## Slide 11: Research in IC CAD Tools/Design Systems
Technology
Process
Device
Geometric
Circuit
Logic
RTL
Behavioral
Systems/Applications
Symbolic Layout
Analog Synthesis
FPGA Tools
Cell Generation
Automated Layout
Logic Optimization
Sequential Machine Opt. and Syn
Module
Generation
Logic Synthesis
Register Allocation
Retiming
RTL Synthesis
HDL Behavioral Synthesis
Process Simulation and
Modeling and Tolerancing
Device Simulation
Circuit Modeling
Back Annotation/
Parasitic Extraction
Circuit Simulation
Analog Simulation
Timing Analysis
Logic Simulation
Verilog
HDL/Behavioral
Simulation
Mixed Mode
Simulation
DRC
LVS
LVS
ERC
BIST
DFT ATPG
Tool
Integration
HDL
Verification
Synthesis
Simulation/Modeling
Verification
Testing

## Slide 12: Technologies
Bipolar (SiGe)
NMOS
CMOS * Main Focus of EE222
GaAs
FinFET (Used for Deep Submicron CMOS)
ModFET
HEMT
Superconductor (Josephson Junctions)
Others
Focus of this class is on studying
  How circuit level parameters interact with technology
  Systems level issues and how overall performance is affected

## Slide 13: Integrated Circuit Technologies – Tradeoffs
Bipolar and NMOS are older technologies
- Many circuit design approaches are directly relatable to BiCMOS, GaAs, and CMOS
Different technologies lean toward different applications
NMOS  high density, medium speed, and medium power
Replaced by CMOS, which is NMOS and PMOS
CMOS  high density, medium speed, and very low power (8 to 12 masks)
Very high density – digital VLSI – dominates technology (1985 to today)
  Some specialized analog functions
GaAs  very high speed and high power ( low density)
  Very high speed digital and analog microwave
Bipolar  high speed and high power ( low density)
  Dominant in the 1970’s (6 to 10 masks)
BiCMOS  high density, high speed, medium power
  Mixed-signal (analog and digital) high speed circuits
  Best of both worlds with added cost

## Slide 14: Digital Technologies – Speed.Power Product
Speed-Power Product
- Useful figure of merit to describe a technology
Speed
(time)
Power
good
PMOS
GaAs
HBT
TTL
Bad
ECL
CMOS
BiCMOS
NMOS
Bipolar

## Slide 15: A Brief History
Electronics + biotechnology, ?
Electronics + nanotechnology, ?
Functionality
Number of devices
First transistor, 1947
First IC, 1959
Multi-core processor, 2001
Eniac, ``the Giant Brain,” 1946
Conceptual transistor, by J.E. Lilienfeld, 1926
Monolithic era
15
Notes: Lilienfeld, Max Planc’s student. It had to take another two decades. In the mean time, we had to deal with vacuum tube based computing.

## Slide 16
Point contact transistor
1947
Junction transistor
1950
Junction field-effect transistor (FET) 1951
Surface barrier transistor
1953
Photolithographic process
mid- 1950s
Oxide masking 1954
Diffused base transistor
1955
Power germanium rectifier
1951
Schottky barrier diode 1960
Impatt diode (silicon) 1964
Zener diode 1952
Silicon controlled rectifier 1957
Metal oxide semiconductor (MOS) FET 1960
Monolithic IC 1958
Planar transistor 1959
Epitaxial transistor 1960
Commercial monolithic resistor-transistor logic 1961
MOS IC
early 1960s
Complementary symmetry MOS (CMOS) 1963
Diode-transistor logic (DTL)
1962
Transistor-transistor logic (TTL)
1962
Emitter-coupled logic (ECL)
1962
Linear IC
1964
Tunnel diode 1957
Commercial silicon junction transistor 1954
Discrete transistors
Power semiconductors
IC’s or immediate predecessors
Microwave and optoelectronic devices
*G. Lapidus, “Transistor Family History,” IEEE Spectrum, pp. 34-35, January 1977.

## Slide 17
D. Kahng and M. Atalla MOSFET invented 1950
D. Kahng and S. Sze Floating Gate (Nonvolatile Memory) Cell Invented 1959– Chesse Cake Inspiration

## Slide 18: Brief History of CMOS
1920
1925
Principle of MOSFET proposed
by Lelienfeld
1947
Bardeen and
Brattain
invent transistor
Dacey and Ross
implement FET
Noyce produces
first fully integrated circuit
Shockley
invents
FET
Kilby makes
hybrid integrated
circuit
1955
1952
Hoerni
develops
planar
process
1962
1960
1965
Burns provides
analysis of
CMOS inverters
Wanlass
develops
first CMOS
inverter
CMOS begins
dominance over
other technologies
IBM PC
announced
1981
Portable
applications
become
popular
IC’s have
5+ million
transistors,
100’s of MHz
2000
2010
Memory:
64 Gigabits/chip
Logic:
100 Million +
transistors

## Slide 19
Evolution of Integrated Systems
Time
2009
19
1946
1947
1958
Monolithic era
A reduction of ≈ 7200 mm2/day in area
A reduction of ≈ 7.5 watts/day in power
An increase of ≈ 100 kHz/day in speed
ENIAC, the “Giant Brain”
  ≈ 18,000 vacuum tubes
  174 kWatts
  ≈ 1800 ft2
  100 kHz
First transistor
First integrated circuit
16-core microprocessor
  410 million transistors
  250 watts
  396 mm2
  2.3 GHz
Notes: Fairchild IC: 4 transistors, one metal layer
Infineon IC: SiP for GSM/EDGE
60s, metal to polycrystalline and self aligned process (http://www.computerhistory.org/semiconductor/timeline/1968-SGT.html)
1963, cmos invented, but not adopted due to performance limit. (http://www.computerhistory.org/semiconductor/timeline/1963-CMOS.html)
Sub threshold mode logic
Dynamic logic

## Slide 20: Evolution of Design Objectives
Area
Power
Speed / Power
Ultra low power
Time
1960s
1980s
1990s
2000s
1970s
5 µm
1 µm
100 nm
2010s
22 nm
Speed / Power /
Noise
  Signal integrity
  Power integrity
  Robustness
Reliability
Predictability
Manufacturability
Speed / Area
Speed
Yield concern
Limited integration
Higher integration
Transition to CMOS
Supercomputers
Subthreshold logic
Nanoscale dimensions
Very high integration
Heterogeneous systems
E. Salman and E. G. Friedman, High Performance Integrated Circuit Design, McGraw-Hill, in preparation
Design process is strongly driven by design constraints
Infineon, monolithic transceiver
Fairchild Semiconductor
20
Notes: EMPHASIS HERE NOISE, AND GO TO HETEROG. SYSTEMS TO MOTIVATE NOISE Important to put the design process into perspective. Starts to behave like pure analog circuits where any two parameters trade with each other. Not surprisingly, the design time has increased. Design productivity.

## Slide 21: Physical Design in a Heterogeneous System
E. Salman and E. G. Friedman, High Performance Integrated Circuit Design, McGraw-Hill, in preparation
Monolithic substrate
Power distribution
(Digital)
Power distribution
(Analog)
Ground distribution
(Digital)
Ground distribution
(Analog)
Clock
distribution
Digital
blocks
Global signaling
Sensitive
blocks
Monolithic substrate
Infineon, monolithic transceiver
Intel, System-on-Chip, Tolapai
Physical design is more than the “layout” of an integrated circuit
Connectivity issue
21
Notes: The device is smaller, much more reliable, but the connectivity problem is still there. That’s one of the most fundamental issues in the physical design, also referred to as interconnect problem. Depending upon our research focus, we see different aspects of these circuits. Assuming it is a synchronous system.

## Slide 22: Implications of Physical Design Objectives
Speed
Power
Area
Global signaling
Clock distribution networks
Power distribution networks
22

## Slide 23: Implications of Physical Design Objectives
Global signaling
Clock distribution networks
Power distribution networks
Speed
Power
Area
Signal integrity
Power integrity
Robustness
Reliability
Manufacturability
Complex tradeoffs
Noise
23

## Slide 24: Electrical “Noise”
Analog/RF
  Device noise
    Shot
    Thermal
    Flicker
    Burst
Synchronous digital
  Switching noise
    Power/ground noise
    Crosstalk
    Delay uncertainty
Mixed-signal
  Substrate coupling noise
    Mitigation
    Efficient estimation
T min
T max
Increased robustness
Enhanced signal integrity
Reliable integration
Injector
Substrate
Receiver
24
Notes: The perception of noise is quite different depending upon the type of circuit. In digital synchronous circuits, when we say noise, we primarily refer to switching noise. In mixed-signal circuits, where we have both digital and analog/RF circuits, coupling from digital to analog/RF becomes crictical. Mixed-signal circuits, 66% of the market today. Since switching noise is one of the primary constraints for physical design, I would like to give some more general background on physical design, and then come back to these problems.

## Slide 25: Power and Clock Distribution
  Topology
  Pad number and location
  Metal width and pitch
  Buffer placement
  Link insertion
  Decoupling capacitor
  Impedance extraction
  Decap estimation
  Load current modeling
  Global simulation
  Timing and power
Analysis
Design
25
Notes: Traditionally area and electromigration, now noise and impedance

## Slide 26: Global Signaling
Circuit block 1
  Topology
  Metal width and pitch
  Signal quality
    Repeater
    Register
    Data recovery
  Impedance extraction
  Driver, receiver model
  Coupled interconnect
  Simulation
Driver
Receiver
Analysis
Design
26
Circuit block 2
Aggressor
Victim
Notes: Larger die area, higher transmission rates, signal integrity. To transfer signal from one signal block to another. Can be on-chip or off-chip. Traditionally, power, speed, still important, but now also noise, noise coupling.

## Slide 27: Substrate Coupling
LNA, data converter, wideband amplifier, bandgap circuit, …
Baseband digital, output buffers, power amplifier, …
Noise reduction
Analysis
  Injector
  Transmission medium
  Receiver
  Substrate extraction
  Power network extraction
  Aggressor circuit
27
Notes: Mixed-signal circuits, if we exclude the pure memory circuits, it is 66% of the semiconductor market is mixed-signal circuits. The nature of the problem has changed.

## Slide 28: Interdependent Physical Design
Loosely-coupled design methodologies produce less optimal circuits than co-dependent methodologies
Monolithic substrate
Power distribution
(Digital)
Power distribution
(Analog)
Ground distribution
(Digital)
Ground distribution
(Analog)
Clock
distribution
Digital
blocks
Global signaling
Sensitive
blocks
Monolithic substrate
28
Notes: Refer to physical design conference. I have already shown how interdependence helps in reducing delay uncertainty. Make sure to continue publishing and pushing papers out. Natural extension of my work. We can improve not only signal integrity but also the performance of the circuit or reduce power dissipation. I have showed an example how considering the interdependence in timing constraints reduced pessimism and delay uncertainty with a more robust circuit. Here is another example of considering codependence.

## Slide 29: Abstraction Level and Physical Constraints
``… to enable more efficient design space exploration, a new level of abstraction is needed …’’ ITRS 2009
``Raising the level of abstraction when designing chips”*
A. Sangiovanni-Vincentelli, “Quo Vadis, SLD? Reasoning About the Trends and Challenges of System Level Design,” Proceedings of the IEEE, March 2007
Physical information
Productivity
Flexibility
How to handle physical constraints at higher levels of abstraction?
Higher level abstraction
Lower level abstraction
29
Notes: Trend for a higher abstraction level to handle complexity and increase productivity. I am not going to develop that abstraction level, but from my perspective, there is an issue here.

## Slide 30: Technology Aware Physical Design
Design engineer
Process engineer
Design for manufacturability
Interconnect design at only two widths: minimum and maximum
  Implications on power-noise-speed-area?
  Compensation at different levels?
30
Notes: There is always this tension between a design engineer and process engineer, although they don’t typically see each other, design engineer wants more relaxed rules, but the process engineer says you cannot do that. Maybe not this bad, but there is definitely a tension. And especially with the manufacturability being a primary design objective. How can we make physical design more technology aware.

## Slide 31: Complexity Requirements of Large Scale Networks
Power/ground networks
  Millions of nodes
  Linear RLC network
Transistors
  Nonlinear
  Complicated device models
Substrate
  3-D RC mesh
  EM extraction
  FDM and BEM
Current
profile
Substrate
Linearize
``the tyranny of numbers’’ *
Jack Morton, Bell Laboratories, 1957
31

## Slide 32: Bottleneck and Design Gap
Co-existence of “new” and “old” technologies
Design gap is expected to further increase
  Circuit and physical level challenges in heterogeneous integrated systems
  Mapping these opportunities to specific design objectives in physical computing systems
Design
Manufacturing
Bottleneck will shift
Design gap
1981
2010
2025
Design productivity
Technology capabilities
32
Notes: As these technologies and devices get more mature, the bottleneck shifts from manufacturing to design, and we cannot wait to develop design methodologies and circuit challenges until it matures.

## Slide 33: Advances in IC Technologies
A journey that started in 1959
First integrated circuit
Fairchild Semiconductor
1959
First microprocessor
Intel 4004
1971
Pentium 4
Intel Corporation
2002

## Slide 34: AT&T BELLMAC-32 TEAM at MH LOBBY (1981)
.

## Slide 35: World’s First 32Bit CMOS Microprocessor BELLMAC-32
.

## Slide 36: Mighty Then

## Slide 37: Technology Scaling
Scaling of minimum feature size
  From 10 um in 1971 to 0.13 um in 2003
4004
i386
8086
Pentium Pro
8080
Pentium
i286
i486
8085
Pentium 4
Pentium 2
Pentium 3
Core
Pentium D
Core 2
Core i7
Notes: 37

## Slide 38: Increasing Die Area
14% per year
  Additional circuitry to enhance performance and functionality
4004
i386
8086
Pentium Pro
8080
Pentium
i286
i486
8085
Pentium 4
Pentium 2
Pentium 3
Core
Pentium D
Core 2
Core i7
Notes: 38

## Slide 39: Increasing Clock Frequency
Enhanced device performance
Innovative circuits and microarchitectures
~ 30,000x
Classical Scaling Era
Modern Era
Multicore
4004
i386
8086
Pentium Pro
8080
Pentium
i286
i486
8085
Pentium 4
Pentium 2
Pentium 3
Core
Pentium D
Core 2
Core i7
Notes: 39

## Slide 40: Microprocessor Power Trends
Power consumption increases
NMOS to CMOS Transition
4004
i386
8086
Pentium Pro
8080
Pentium
i286
i486
8085
Pentium 4
Pentium 2
Pentium 3
Core
Pentium D
Core 2
Core i7
8008
Notes: 40

## Slide 41: Power Density Trends
Power dissipation
Hot spots
Cost of cooling
  Low cost cooling
    Air flow fans
    Heat sinks
  Expensive cooling solutions
    Liquid cooling
    Refrigeration
Hot Plate
Nuclear Reactor
Rocket Nozzle
4004
i386
8086
Pentium Pro
8080
Pentium
i286
i486
8085
Pentium 4
Pentium 2
Pentium 3
Core
Pentium D
Core 2
Core i7
Power Wall
Notes: 41

## Slide 42: Supply Voltage Scaling
Enhanced device reliability
Reduced power consumption
Classical Scaling Era
Modern Era
12 Volts
5 Volts
3.3 Volts
1.5 Volts
4004
i386
8086
Pentium Pro
8080
Pentium
i286
i486
8085
Pentium 4
Pentium 2
Pentium 3
Core
Pentium D
Core 2
Core i7
Notes: 42

## Slide 43: Increasing Supply Current
Higher power at a lower supply voltage
   Generation
   Distribution
NMOS to CMOS Transition
Power Wall
4004
i386
8086
Pentium Pro
8080
Pentium
i286
i486
8085
Pentium 4
Pentium 2
Pentium 3
Core
Pentium D
Core 2
Core i7
Notes: 43

## Slide 44: Supply Voltage Scaling
Enhanced device reliability in a scaled CMOS technology
Reduced power consumption
0.01
0.10
1.00
10.00
0.8
1.0
1.2
1.4
1.6
1.8
2.0
2.2
2.4
2.6
2.8
3.0
V
DD
(V)
Power (normalized)
103 X
24 X
3.8 X
2.3 X

## Slide 45: Increasing Propagation Delays
Circuit speed degrades
VDD (V)
0
1
2
3
4
5
0.8
1.0
1.2
1.4
1.6
1.8
2.0
2.2
2.4
2.6
2.8
3.0
Delay (normalized)
V
DD
= 1.8 V
6.3 X
4.4 X

## Slide 46: Supply Voltage Scaling
More than quadratic reduction in the dynamic switching power
  Switching frequency is reduced
More than linear reduction in the leakage power
  Subthreshold leakage
  Gate oxide leakage
V
DD
0
IGate-oxide
V
DD
C
L
I
Subthreshold
V
DD
C
L
I
Load

## Slide 47: Emerging Technologies (Beyond CMOS)
Emerging devices and technologies
Device level
  Carbon nanotubes
  Graphene based devices
  Multi-gate devices
  Resistive memory
  Memristors
Technology level
  3-D integration
  System-in-package
  On-chip optical interconnects
Power - speed
wall
Technology wall
Noise wall
47
Notes: From my perspective, the circuit and physical level challenges of these emerging devices and technologies is important. Scaling is expected to continue for another decade, but there are also emerging devices and techs. I will be interested in the circuit and physical level challenges of these new devices and technologies. of the Benefits of scaling is likely to end. Alternative opportunities. Gap further increases with the introduction of 3D, SiP, and other emerging opportunities…
Mention some 3d physical design challenges

## Slide 48: Summary
Physical design challenges
Speed
Power
Area
Signal integrity
Power integrity
Robustness
Reliability
Manufacturability
Design automation
Design methodologies
Specialized circuits
Heterogeneous integrated systems
48
Noise
Synchronous digital
Mixed-signal
Delay uncertainty
Substrate coupling
Noise
Notes: I summarized some of the challenges in the physical design, especially with the emergence of new design constraints. I presented some of our research results related to increasing the robustness and efficiently estimating substrate coupling noise which is important for improving signal integrity. Finally, I proposed a framework for future research which has three domains. 1, 2, and 3, for heterogeneous embedded systems.

## Slide 49
Evolution of IC Design Objectives
Area
Time
1970s
1980s
1990s
2000s
Speed / area
Power
Ultra low power
Speed
Speed / power
Speed / power / noise
Ultra low power
M. Popovich, A. V. Mezhiba, and E. G. Friedman, Power Distribution Networks with On-chip Decoupling Capacitors, Springer Verlag, 2008
Yield concern
Limited integration
Intel 4004
Intel 386
Higher integration
New applications
Intel Pentium
Three paths of design objectives
Very high integration
Complex SoCs
RF, analog, and digital on the same die
Multi core era
Notes: Advances in the fabrication technology 2) emergence of new applications
60s and 70s: Yield concern is the primary limitation to integration density. Therefore, circuit compactness and area were the primary design objectives. Due to limited integration density, a typical system was composed of many small integrated circuits where the performance was limited by the inter-chip communication.
Due to the advances in the fabrication technology, system speed became a stronger function of the single ICs. Therefore, in 80s,
Speed gained a very high priority as a design objective. At the same time, a new set of applications emerged where power also became very important. These applications include digital wrist watches, handheld calculators, and some satellite electronics.
Later in 90s, with even higher integration, speed and power had to be considered at the same time, resulting in three different paths of design objectives. Ultralow power where speed is not important. Very high speed applications where power is tolerated and those applications where speed and power are optimized at the same time.
Starting 2000, the primary trend was to integrate different functions on the same die such as analog, RF, and digital to reduce the overall cost. A new design metric emerged which was noise.

## Slide 50: Design Goals of CMOS Integrated Circuits
2000’s
Speed/Power/Noise
1970’s
Area
1980’s
Speed/Area
Power
Ultra-Low Power
Speed
1990’s
Speed/Power
2010’s
POWER/Noise/speed

## Slide 51: Speed/Performance Issues
Al 3.0  - cm
Cu 1.7  - cm
SiO2  = 4.0
Low   = 2.0
Al & Cu 0.8 m Thick
Al & Cu Line 43 m Long
Gate and interconnect delay versus technology generation
The National Technology Roadmap for Semiconductors, 1997

## Slide 52
Evolution of IC Design Objectives
Time
1960s
1980s
1990s
2000s
M. Popovich, A. V. Mezhiba, and E. G. Friedman, Power Distribution Networks with On-Chip Decoupling Capacitors, Springer Verlag, 2008
1970s
1959
2008
Area
Speed / area
Power
Speed
Speed / Power
Ultra low power
4 µm
0.8 µm
0.1 µm
2010s
0.045 µm
Yield concern
Limited integration
Higher integration
New applications
Transition to CMOS
Supercomputers
Subthreshold logic
Very high integration
Complex SoCs
RF, analog, and digital on the same die
Speed / Power / Noise
52
Notes: Fairchild IC: 4 transistors, one metal layer
Infineon IC: SiP for GSM/EDGE
60s, metal to polycrystalline and self aligned process (http://www.computerhistory.org/semiconductor/timeline/1968-SGT.html)
1963, cmos invented, but not adopted due to performance limit. (http://www.computerhistory.org/semiconductor/timeline/1963-CMOS.html)
Sub threshold mode logic
Dynamic logic